Determination of hydroxymethylfurfural (HMF) by HPLC

Theory:

Determination of hydroxymethylfurfural in honey is used to determine it`s temperature history. HMF is not practically presented in fresh honey. It is naturally generated by heat-treatments and longer storage of honey under inappropriate conditions.

- storage of the honey at higher temperature

- inconsiderate heating (in order to avoid crystallization by dissolution of sugar crystals).

HMF is formed from sugars, mainly from fructose as a product of Maillard´s reaction.

The EU limit: maximum of 40 mg/kg

The limit of the norm “Czech Honey”: maximum 20 mg/kg

Principle:

HMF is determined in the clear, filtered aqueous honey solution by reverse phase HPLC with UV detection at a wavelength of 285 nm.

Equipment:

- HPLC with UV detector

- C 18 column with reverse phase

- membrane filters 0,45 (m

Procedure:

- weigh 5 g of honey with an accuracy of at least 2 decimal places into a 25 ml beaker (for calculation the HMF content is important to note weight) and add about 15 ml of HPLC water. ATTENTION: use only HPLC water!

- dissolve the sample and transfer it quantitatively into a 25 ml volumetric flask and fill with HPLC water up  to the mark and mix well

- transfer this solution into a 50 ml beaker

- filter this solution through a membrane filter into HPLC vial, sign the vial with sample ID

- HPLC measuring

Calculation:

The concentration is determined by the external standard method. Obtained concentrations in mg/l (= c1) is necessary to convert to mg/kg (= c).

Dilution factor F = total sample volume [ml] / sample weight [g]

c = c1 * F